## Slide 3: Load carrier
Requirements for unit load
  High concentration of goods flow
  The flow of goods must be regular
  The logistics chain can contain several means of transport
Application
  Standardized load carriers
    Container, Trailer
    Can be used intermodally
      Lake, road and rail

## Slide 4: Load carrier
Type 20' TEU DV
  Twenty-foot Equivalent Unit
  Dry van
  LxWxH ext 6058x2438x2591
  LxWxH inv approx 5900x2350x2370
  Palletwide 2.44 wide
  Volume 33 m3
  Tare weight approx. 2200 kg
  Cargo cap . approx. 21800 kg

## Slide 5: Load carrier
Type 40' (= 2 TEU )
  LxWxH ext 12192x2438x2591
  LxWxH inv approx 12050x2350x2370
  Palletwide 2.44 wide
  Volume 67 m3
  Tare weight approx. 3900 kg
  Cargo cap . approx. 26600 kg
type 45'
  Length 13.7m
High cube
  Height 2.69m
  40' and 45'
Containers in all sizes are also available for refrigerated and frozen goods

## Slide 6: Cargo carrier flight
ULD
  Unit Load Device
  Airline property
  Companies that rent out
  Used only in the air transport system

## Slide 7: Load carrier
Car & trailer
Outer dimensions :
  Height: 4.2 m Width: 2.6 m Length: 24-25 m
  Number of axles: + 5
Approx. Inner dimensions:
  Height: 2.95 m Width: 2.48 m Length: 20.0 m
  Total weight = load and vehicle 60,000kg – 74,000kg
  Load capacity: 40,000 kg – 50,000 kg

## Slide 8: Load carrier
HCT vehicle – High Capacity Transport
New law 31 August 1 December 2023

## Slide 9: Load carrier
HCT vehicle – High Capacity Transport

## Slide 10
Total weight of cargo + vehicle
Total weight of cargo + vehicle
Total weight of cargo + vehicle
60 – 74 tonnes
18.75 m
HCT vehicle – High Capacity Transport
Picture: Dan Boman Scania CV AB
2 40' (foot) containers = 2 x 12 meters
Vehicles with three trailers
7.82m + 7.82m + 13.6m
Notes: 27% less fuel and CO2 emissions

## Slide 11
18.75 m
HCT vehicle – High Capacity Transport

## Slide 12
HCT vehicle – High Capacity Transport
590 miles of state roads from 1 Dec 2023

## Slide 13: Load carrier
Road transport
Trailer
  Outer dimensions Height: 4.0-4.2 m Width: 2.55 m Length: 13.9 Inner dimensions: Height: 2.7 Width: 2.48 m Length: 13.6 m Load capacity: 26,000 kg
  Permitted weight in Europe 24,000kg
  Length including tractor
    18.75 m

## Slide 14: Load carrier

## Slide 15: Load carrier
Trailer Double-decker

## Slide 16
Forwarder/ Logistics company
Hauling
Ports
Collaborative partners outside Sweden
Freight terminals/ Hubs
Train operator
Airline
Shipping company
Collaborative partners within Sweden

## Slide 17: Freight companies
The business
  Transport manager
  Geographic areas
  Vehicle
  Driver

## Slide 18: Terminal system and transport system domestically
Hauliers domestic transport
  Bid transport – Freight transport
  Single car rider – Multiple vehicles
  Operation
    Subcontractors
      DHL, Schenker, DSV etc
    Included in network
      Intermediary
        For example, the Transporter
      Connected to LBC, Lastbilscentral
        E.g. GLC Göteborgs Lastbilscentral
    Has transshipment terminal

## Slide 19: Freight companies
Local transport
Distribution
Long-distance transport
Tow truck operation
International haulage companies
Food
  Refrigerated and frozen transport
Construction and construction
Cleaning
Special transport
Agricultural transport
  Animal transport
Tank transport
Log transport

## Slide 20: Freight companies
The business
Local distribution
  In cities
  Smaller geographic areas
  Smaller vehicles
  Light Truck
    Total weight up to 3500kg
    Load weight approx. 1000kg
  Heavy truck
    Total weight 23000kg
    Load weight approx. 7600kg
    About 6 pallets

## Slide 21: Freight companies
The business
Long-distance transport
  Transport between cities
  Vehicle
    Car and trailer 24 - 25m
    Trailer 13.6m
    HCT vehicle
      Up to 34.5 m
  Consolidation
    Many companies' goods
    To/From the same area/city

## Slide 22: Freight companies
The goods owner's transport needs
  Package
    < 100 kg
  General cargo
    < 2500 kg
  Party goods
    > 2500 kg
  Hellest, full car
    > 20,000 kg

## Slide 23: Freight companies
Packages and piece goods

## Slide 24: Freight companies
Bulk goods 2500kg – approx. 18,000kg
  Loaded at the sender
  Unloaded at the receiver
  Same vehicle
  Door/Door
Hellest
  The goods owner books the entire load carrier

## Slide 25: Freight companies
Tow truck operation
  Loose trailer system
    Often used in international traffic
  Vehicles without load carriers
  The load carrier is owned by
    Forwarding agent
    Logistics company
  The load carrier
    13.6m trailer
  Driver
    Employees of the haulage company
  The assignments
    Comes from forwarders and logistics companies

## Slide 26: Freight companies
Towing companies
  Container
  Chassis
  One chassis = 2 x 20ft alt 1 x 40ft
  (20ft = 6m long 40ft = 12m long)

## Slide 27: Freight companies
Towing companies
  Swimming lift
    Chassis with crane
  Possibility to take off
  Used when there is no loading dock

## Slide 28: Freight companies
International haulage companies
  Whole crew
    Owns tractor and trailer
    Principal
      Forwarders
      Logistics company
      Goods owner
    Specialized
      Geographic areas